## Slide 1: Wireless download with Network Odin

## Slide 2: Revision History
Version | Date | Contents | Author | Reviewer
0.6 | 2015-03-09 | Initial Version for factory process | Gwiro Lee | Donghoon Ryu
1.0 | 2015-04-15 | Adding SoftAP and Troubleshooting | Jayoung Gu Gwiro Lee | Jaekil Jeong
1.1 | 2015-08-29 | Update “Enter Reboot Mode” (Page. 4) | Jaehoon You | Jaekil Jeong

## Slide 3: Contents
Wireless Download
  Setup Environment and Enter REBOOT MODE
  Run the soft AP at WC1
  Search and Select the SSID in PC
  Check the connection between Odin and WC1
  Download binaries
Troubleshooting
[Appendix]
- Wireless Download for Factory Process

## Slide 4: 1. Wireless Download (1/5)
  Setup Environment and Enter REBOOT MODE
Setup Environment
  It’s OK if you can use wi-fi in your PC
Run the NetOdin3 on your PC.
Enter REBOOT MODE in WC1
  Press and Hold the Power Key for 7 seconds
  Press Power key three times shortly when you see rebooting screen (refer to picture-1)
  Press Power key four times shortly then you can move to “Download (wireless) menu. (refer to picture-2)
  Press and Hold Power key for 3 seconds
Power Key Control Guide
  Short Press : Move
  Long Press : Select
picture-1
picture-2

## Slide 5: 1. Wireless Download (2/5)
  Run the softAP at WC1
  Double-click the Power Key
  Then you can see the SSID of softAP on WC1
  (refer to picture-2)
picture-2

## Slide 6: 1. Wireless Download (3/5)
  Search and Select the SSID in PC
  Search and Select the SSID which is displayed on WC1 in your PC
[Search the SSID in PC]
[Select the SSID in PC]

## Slide 7: 1. Wireless Download (4/5)
  Check the connection between Odin and WC1
  You can see WC1’s IP on Odin and the leased IP to PC on WC1 if Odin and WC1 are correctly connected via wi-fi.

## Slide 8: 1. Wireless Download (5/5)
  Download binaries
  Enjoy your wireless download !!!

## Slide 9: 2. Troubleshooting
  If you encounter a problem while downloading…
  Please try to check the below list.
  There are no tips to be applied, please report it to Tizen R&D Team.
    Kyu-Wook Lim(kyuwook.lim@samsung.com)
    Jaehoon You(jaehoon.you@samsung.com)
No. | 문제 구분 | 문제 현상 | 원인 | 해결 방안
1 | Windowns PC | PC에 무선랜 어뎁터는 있는데, 사용가능으로 설정 안됨 | ESCORT에 의해 dafault로 무선랜이 사용불가능으로 설정되어 있음 | 무선랜 예외 신청
2 | Windowns PC | 정상적으로 AP 연결되었으나 Odin과 연결이 되지 않을 경우 | 무선랜 인터페이스가 static ip로 설정된지 확인 필요 (ipconfig시 192.168.49.20 인지 확인) | static ip를 "자동으로 ip 받기"로 설정되었는지 확인 필요
3 | Windowns PC | 정상적으로 IP 할당 되었으나 Odin과 Gear가 연결되지 않는 문제 - Windwos PC에서 Odin으로 Ping은 나가지만, - 외부에서 Windows PC로 Ping은 들어오지 않음 | Windows 방화벽에 의해 외부 접속을 reject함 | - 설정 -> 제어판 -> windows 방화벽에서, 공용 네트워크의 Windowns 방화벽 사용 안함 설정 - V3 -> 개인방화벽 사용안함 설정
4 | Windowns PC | 유선랜으로 인터넷 연결중 무선랜으로 바이너리 다운받는 경우 PC 에서 인터넷 접속안되는 이슈 (AP Mode) | tcp/ip의 matrix 설정 문제 https://support.microsoft.com/ko-kr/kb/299540/ko) | 로컬 영역 연결 -> TCP/IPv4 속성 -> 고급 -> 기본 게이트웨이 편집 -> 자동 메트릭 체크 해제, matrix '5' 입력 확인
5 | Windowns PC | 무선랜 연결 후, Odin을 늦게 실행 하거나 Odin을 종료 후 실행 했을때 자동 연결되지 않는 문제 | windows 방화벽 사용하지 않음으로 설정하더라도 인바운드 설정 필요 | 제어판->Windows 방화벽->고급설정->인바운드 규칙->새 규칙 에서 프로그램에 Odin을 추가
6 | Windowns PC | NotePC로 Gear 시료의 AP를 검색 후 연결하였을 때, 무선랜 ip가 192.168.49.20로 설정 안되는 문제 | uready나 기타 다른 AP를 빈번히 사용할 경우 windows pc에서 ip 갱신을 못하는 경우가 발생할 수 있음 | 윈도우 pc에서 ipconfig/release, ipconfig/renew를 통해 자동 갱신하도록 한다

## Slide 10: Appendix

## Slide 11: Wireless Download for Factory Process (1/3)
Connect Host PC to Wireless AP via UTP cable
  WPS button is needed in AP.
Change the IP on Host PC
  IP : 192.168.0.111
  Netmask : 255.255.255.0
Start Odin and wait for connection

## Slide 12: Wireless Download for Factory Process (2/3)
Press and Hold your Power Key and enter REBOOT MODE in WC1
Choice “Download (wireless)” menu
  Power Key Control Guide
    Short Press : Move
    Long Press : Select
Press WPS button on the wireless AP
After a while, WC1 will be connected with wireless AP
[WC1]
[Access Point]

## Slide 13: Wireless Download for Factory Process (3/3)
You can see the connected IP through Odin, if there is no problem
Now, you can start download on the WC1
  Currently, the changing of PIT file is not supported in the wireless download mode.
  If there is a changing of PIT file, please use USB Odin downloader.

## Slide 14: Thank you.